Silver water ionizer Nevoton IS-112 (Невотон ИС-112)

Nevoton IS-112 is designed to generate the silver anions water solution (Ag+) at home.

Silver anions deposit during the passing of direct current between two electrodes. On of them is made from fine silver (999,9), the other one – from stainless steel.

Ionizer is controlled by digital microprocessor, that adjusts current parameters and operation cycle time subject to purpose and solution volume. Digital technology application provides fail-safety and extra precise operation of device.

Who to use ionizer

Nevoton IS-112 is very simple and easy to use.

Put it on top of a jar. The capacity of the jar may be 1, 2 or 3 liters.

Control panel with three sensor buttons is located on the top of ionizer case.

“Режим” button – adjusts the concentration of solution (“POTABLE” or “CONCENTRATE”).

“Объем” button – adjusts the volume of work liquid (one/two/three liters).

Chosen modes are imaged by respective indicator.

“Пуск/стоп” button – starts and early stops ionization in case of necessity.

During the ionization indicator of work is lighting evenly.

The ending of ionization is automatic. If the indicator above “пуск/стоп” button is flashing and every 10 seconds rings short sound signal – the process of ionization is ended.

Your silver water is ready!

After the ending of ionization push “пуск/стоп” button. Ionizer transfers to initial state (POTABLE/ 1 liter) and ready for new startup.

Time of water processing is adjusted automatically under regime and water volume selecting.

| Volume | Potable | Concentrate |
| --- | --- | --- |
| 1liter | 35 sec. | 20 min. |
| 2 liters | 70 sec. | ------- |

Two kinds of “silver” water.

Ionizer Nevoton allows to prepare two kinds of water.

Potable – water with silver ions concentration 35mcg/liter. Such water is permitted for food. It’s useful in cooking, prolonging marinade, pickles and jams keeping time.  You could treat toys and dishes to eliminate bacteria from surfaces.

Concentrate – water with silver ions concentration 10000 mcg/liter. You could use this water for washing, cosmetics, flowers watering, fruits and vegetables washing.

Do not use this water in food!

Concentrate-regime leads to great discharge of silver electrode. So, we recommend to use this regime economically.

For this reason ionizer program doesn’t  provide volume selection. You can prepare only 1 liter of water for one time.

Quality of silver water depends on initial mineral composition. That’s why, for getting magnificent silver water we recommend to use potable non-mineralized water in bottles. Do not use distilled water!

Specifications

Concentration of product solution:

Potable-regime – 35 mkg/L

Concentrate-regime – 10000 mkg/L

Useful operating life of electrode in potable-regime: over 60000 liters

Voltage: 220V

Output voltage: 12V

Output current: ~ 100 mA

Power consumption: ~ 5W

Dimensions: (mm) 125 x 125 x 150

Weight:  600 g 
Silver electrode weight: 2,7 g

Method of operation

- Prepare container with water.

- Switch on.

- Place ionizer into the container (electrodes have to be completely dipped into the water).

- Select the regime.

- Select the volume.

- Push the “Стоп/пуск” button for starting ionization process (over the button will light an indicator).

- The end of ionization is signalized by flashing indicator and every 10 seconds rings a sound signal.

- Ionization is over. Put product solution into the clean capacity.

During ionizer working on it’s surface and walls accumulate silver ions and form grey deposit. This deposit could form electric bridge between electrodes. It will lead to closedown of ionizer. That’s why you have to regularly clean the surfaces of electrodes by special brush.

Fordidden:

To put upper part of ionizer into the water.

To turn ionizer by holder with electrodes upward.

To switch on by wet hands.

To keep ionizer in capacity with water.

Healthy properties of silver

For today It’s hard to say, how long time ago mankind found out curative properties of this noble metal. Well known, that  2500 years before Christ Egyptian warriors used silver for treatment of battle wounds – putted  very thin plates on them, and wounds healed very fast. It’s conditioned by bactericidal properties of silver.

Most active elements of silver are it’s ions. This active ions could be taken during process of electrolysis in water medium by special device. Ionizer Nevoton provides optimal concentration of active ions for home using.

Active silver ions easily penetrate into the living organism tissues and circulate in blood and fluid medium. If they meet pathogen microbes, viruses or fungi - likewise pass trough their outer shell and cause death.

Quantity of silver in tissues of human organism reaches 20 mcg on 100 g of dry matter. Most of it is accumulated in brain, nervous cells, endocrine glands, iris and bones. Silver is an essential structural element of our tissues.

Silver ions stimulate blood-making organs, intensify metabolic processes in brain, that improve it’s function. They take part in metabolism and consumes, so we have to additionally  supply it from without. Usually silver come into the organism with food – cucumbers, cabbage, dill. But concentration of silver in that vegetables is very small. On the other hand, if you drink a glass of silver water everyday, you quite supply your organism need in silver.

Silver is an essential microelement, that provides our health. It saves us against the infection - silver ions take part in functioning of our immune system. Also it has a bactericidal properties.
    
Minimal concentrations of silver in “silver” water (0.01 mg/L) are sufficient for destructing various pathogen microbes, viruses and fungi. In autumn and winter preventive use of silver water helps to resist catarrhal adenoviruses, influenza and parainfluenza. In summer it increase resistance to enteric infection without dysbacteriosis

Beauty and health

Silver water possesses rejuvenating, anti-inflammatory and balancing action on skin of face and body. That’s why cosmetologists recommend daily washing with silver water. It reinforces hair, that is weakened by chemical and mechanical aggression. Inflammatory processes stop, hair growth become more active. If you want to save your health and beauty, get rid of tiredness and head pains – take a “silver” bath with “silver” water. It dilates your capillaries, stimulates cells activity, normalizes hormone levels, increases immunity, removes poisons and chemical waste.

For taking care of face use silver water, made in concentrate-regime. If you don’t use all volume of water, we recommend to keep the remains in the refrigerator for future applications. Next time mix it thorough before using.

House and garden    Silver water (concentrate) is successfully used by gardeners for increasing and saving of harvest, for activating plant’s immunity against microorganisms, for prolongation a cut flowers life.

Plants and seedling watering

Silver water decontaminate soil. For plants watering use next solution: 200 ml concentrate-regime silver water dilute in 10 liters of water.

Plants spraying    Plants spraying with silver water decrease fungal infections. Use silver water as stated for watering.

Long-term preservation of cut flowers

Silver water allows to prolonging cut flowers life. Use water as stated for watering. Change it every day by makeup water.

Use silver water with air humidifier    If you use air humidifier, you can apply silver water. It will make the atmosphere of freshness and cleanness in your house. Put humidifier among plants, and they will gladden your eyes with gross leaves and splendid flowers.

Furniture and door handles     Well known, that there is a great number of bacteria are located on door handles, and every day we contact them. Regular processing of this surfaces by Concentrate significantly decrease the risk of infection. It’s especially actually, when someone is ill at home.

Disinfection of sanitary rooms       Bathroom and toilet always need more thorough sanitary processing. Silver water perfectly manages with this task. All you need – is to prepare 1 liter of silver water in Concentrate-regime.

Toys processing   Kiddies strive to taste anything, especially their toys. Toys washing by chemical solutions is not the best solution, because they can came to mouth too. In this case, processing with silver water in Potable-regime can solve the problem.

Dish processing

It’s useful to rinse forks, spoons, plates with silver water. Make enough volume of silver water and rinse it after washing to protect from bacteria.